Notes
Components: For the flight computer, there are some critical parts we need, we need to compare with the reference project, cross check its availability in turkiye and see the replacements.

Component	Ref. component	Replacement(if needed)
MCU	STM32F405RGT6	STM32F446RET6
IMU/GYRO	MPU6000	MPU9350

MCU:
As the reference component cannot be found easily, which is STM32F405RGT6, we need to work with STM32F446RET6. They are both from the F4 family, so we need to check the pin-outs and other requirements for operation. we need to keep looking at their physical specs.

  STM32F405RGT6	STM32F446RET6
The chips are very close to each other but the core differences are:

Feature	STM32F405RGT6	STM32F446RET6
Core Speed	168 MHz (210 DMIPS)	180 MHz (225 DMIPS)
Flash Memory	1 MB (1024 KB)	512 KB
SRAM	192+4 KB (incl. 64KB CCM)	128 KB
SPI Interfaces	Up to 3	Up to 4
I2C Interfaces	Up to 3	Up to 4
UART/USART	6 total (4 USART, 2 UART)	6 total (4 USART, 2 UART)
USB	OTG FS/HS	OTG FS/HS (with dedicated power rail)
Package	LQFP64 (10x10 mm)	LQFP64 (10x10 mm)

Pin layouts:
STM32F405RGT6	STM32F446RET6

For the replacement in pin 47, where the VCAP_2 is replaced by VSS, we should remove the 100nF capacitor and directly connect it to the ground.

We will compare the Alternate function table next: