Notes
Components: For the flight computer, there are some critical parts we need, we need to compare with the reference project, cross check its availability in turkiye and see the replacements.

Component	Ref. component	Replacement(if needed)	Better
MCU	STM32F405RGT6	STM32F446RET6	STM32F407VET6 (100 pin version of ref)
IMU/GYRO	MPU6000	MPU9350

MCU:
As the reference component cannot be found easily, which is STM32F405RGT6, we need to work with STM32F446RET6. They are both from the F4 family, so we need to check the pin-outs and other requirements for operation. we need to keep looking at their physical specs.

  STM32F405RGT6	STM32F446RET6
The chips are very close to each other but the core differences are:

Feature	STM32F405RGT6	STM32F446RET6
Core Speed	168 MHz (210 DMIPS)	180 MHz (225 DMIPS)
Flash Memory	1 MB (1024 KB)	512 KB
SRAM	192+4 KB (incl. 64KB CCM)	128 KB
SPI Interfaces	Up to 3	Up to 4
I2C Interfaces	Up to 3	Up to 4
UART/USART	6 total (4 USART, 2 UART)	6 total (4 USART, 2 UART)
USB	OTG FS/HS	OTG FS/HS (with dedicated power rail)
Package	LQFP64 (10x10 mm)	LQFP64 (10x10 mm)

Pin layouts:
STM32F405RGT6	STM32F446RET6

For the replacement in pin 47, where the VCAP_2 is replaced by VSS, we should remove the 100nF capacitor and directly connect it to the ground.

We will compare the Alternate function table next:

I found a great alternative, I will use STM32F407VET6
The only difference of this die compared to the reference is that it has a larger footprint, with 100 pins, mostly GPIO that can be later used for other things in later upgrades.

This is a game changer as this has exabtly same spec as the reference chip and thus requires minimal rewiring as far the main MCU is concerned.
MPU:
we will be using the MPU-9250 extracted from an old navio2 instead of a MPU-6000. The 9250 IC is much powerful and actually has more features such as magnetometer for compass and more(ref to datasheet). We need to check the pins with 6000 to make sure we understand the differences and connect them accordingly.

MPU-6000	MPU-9250

Pin in 6000	Pin in 9250	What to do in 9250 schematic
Pin-1 CLKIN	Pin-1 RESV	As pin 1 clkin in 6000 ref is connected to GND, its not used. / In 9250 → pin 1(RESV) → VDDIO
Pin -8 /CS	Pin - 22	Shifted from 8→22 in 9250
Pin -20 CPOUT	Pin- 20	In 9250, pin 20 → GND(no 2.2nF)
Pin 6, 7 I2C com	Pin 7, 21 I2C	Not connected, not using Magnetometer for compass